Keynote by A. ASENOV, Device Modeling Group, Glasgow University, UK

"Interaction between physical, compact model and circuit simulation of statistical variability"

Absract - The variability of transistor characteristics has become a major concern associated with CMOS transistors scaling and integration. It already critically affects SRAM scaling, and introduces leakage and timing issues in digital logic circuits. The variability is the main factor restricting the scaling of the supply voltage, which for the last four technology generations has remained virtually constant, adding to the looming power crisis.

In this talk we focus on statistical variability, which has become a dominant source of variability for the 45nm technology generation and which cannot be reduced by tightening process control. We start with the TCAD simulation of statistical variability that helps the design of transistors with reduced variability and the screen new device architectures in terms of their variability reduction potential. TCAD of variability in the early technology development cycle can help to develop accurate and realistic compact models at the PDK stage improving the quality of the design process. Finally the forecast of the statistical variability few technology generations ahead is of great importance for the development of new variability resistant design strategies and corresponding EDA tools. We will discuss also the impact of different compact model strategies on the accuracy of the statistical circuit simulation and verification.  The talk will be illustrated with simulation results of statistical variability in conventional and novel MOSFET architectures scaled according to the prescriptions of the ITRS.

Asen Asenov received his MSc degree in solid state physics from Sofia University, Bulgaria in 1979 and the PhD degree in physics from The Bulgarian Academy of Science in 1989.

He has ten years of industrial experience as a head of the Process and Device Modelling Group in Institute of Microelectronics, Sofia, developing one of the first integrated process and device CMOS simulators IMPEDANCE. In 1989–1991 he was a Visiting Professor at the Physics Department of Technical University of Munich, Germany. He joined the Department of Electronics and Electrical Engineering at the University of Glasgow in 1991, and served as a Head of Department in 1999-2003.

As a professor of Device Modelling and a Leader of the Glasgow Device Modelling Group he directs the development of 2D and 3D quantum mechanical, Monte Carlo and classical device simulators and their application in the design of advanced and novel CMOS devices. He has pioneered the simulations of statistical variability in nano-CMOS devices including random dopants, interface roughness and line edge roughness. He has over 510 publications and more than 160 invited talks in the above areas.

Dr Asenov is a fellow of the Royal Academy of Scotland, a member of the IEEE Electron Device Society Technology Computer-Aided Design Committee and a co-author of ENIAC SRA. He is General Chair for SNW2008, TPC co-chair of ESSDERC2008 co-director of the SINANO/PULLNANO Device Modelling Summer School, and a member of the programme committees for IEDM, ESSDERC, IWCE, SNW, HCIS and DATE.