## Slide 1
Design and Development of a Surgical Simulator
PhD Daniela D’Auria
Tutor: Prof. Bruno Siciliano
Visiting scholar at the University of Washington under supervision of the Prof. Blake Hannaford

## Slide 2
In order to improve the open surgery performances:
Cricothyrotomy simulator for procedural skill training : best choice in low resource environments
Anatomy
Trachea: cylindrical tube
thyroid cartilage - structure in and around the trachea
cricoid cartilage - the only complete ring of cartilage around the trachea
18-22 cartilaginous rings
Preparation: extend and prepare the neck
Palpation: palpate landmarks
Incision
Traction
Intubation
Standard method

## Slide 3
Simulator Design-top view

## Slide 4
Simulator Prototype
Fig. 1- Simulator including mock-trachea, wired sensor interface, LED matrix-based display mounted to an Arduino Uno, drawing power through a USB cable connected to a laptop (out of view). Pads of conductive alluminium foil are connected to input pins on the microprocessor. The instruments (scalpel, hook and kelly forcepts) are connected by a wire to a pin of the microcontroller.

## Slide 5
Experimental results
Graphic results
Pad C represents the correct sheared zone
The correct sequence of touched instruments
is: Scalpel-Kelly Forcepts-Hook (Blue-Red-Red/Green)
B
DEVICE 2
DEVICE 1
DEVICE 3
A
B
D
C
E
F

## Slide 6
Experimental results
Video results
One of the video of the experimental collection

## Slide 7
This surgical procedure simulator is powerful and precise; it is coupled to a microprocessor for:
  recording a medical procedure and assessing that performance for skill
  giving an opportunity to educate users on the cricothyroidotomy procedure
  giving real-time feedback for training or automatic post-performance evaluation
Designed to be built in low-resource environments using common tools and available materials
Next step: create a website with the instructions to build the system, the models, and the training and assessment curriculum
Open issues and further improvements

## Slide 8
Thank you very much!
PhD Daniela D’Auria
Tutor: Prof. Bruno Siciliano