## Slide 1: Innovative actuation and sensing mechanisms for minimally invasive robotic surgery
Supervisors
Prof. Paolo Dario
Prof. Arianna Menciassi
Dr. Eng. Giuseppe Tortora
Research area
Iris De Falco
1st year PhD student in BioRobotics

## Slide 2
STIFFness controllable Flexible and
Learn-able Manipulator for surgical OPerations
www.stiff-flop.eu
Biological Insights
High dexterity and maneuverability
Lack of rigid skeletal support
Meshed longitudinal and transversal muscles
Able to bend in any direction, elongate and
change stiffness at any point along the arm
Technical Solutions
- Modular structure
Soft actuators
Granular Jamming
Medical Requirements
Pass through a 20 mm port
Length of up to 300 mm
Controllable stiffness
Force of at least 1 N (better if 5 N)
A tool on the tip able of exerting a force up to 10 N

## Slide 3
Stiffening Channel
Functional Unit
Flexible Silicone Actuators
Ø 35 mm
Ø 25 mm
Ø 8 mm
R 4 mm
30 mm
50 mm
External Sheath

## Slide 4
Performance of the Single Unit
Bending
Elongation
Force
1 actuated chamber: 24.6 N
3 actuated chambers: 41.4 N
Stiffening
1.5 psi vacuum pressure:
stiffness increasing of 36 %
Squeezing
Diameter decreasing
of 40 %

## Slide 5
Actuation Tubes MODULE 1
Actuation Tubes MODULE 2
Actuation Tubes MODULE 3
Multimodule Integration
19 cm
2.5 cm
Pneumatic tubes
Stiffening vacuum line
External Braided Sheath

## Slide 6
Thank you for the attention
!