## Slide 1: Development of a sensorized platform for implantable cardiovascular applications
Supervisors
Prof. Paolo Dario
Dr. Eng. Monica Vatteroni
Research area
Rossella Fontana
1st year PhD student in BioRobotics

## Slide 2
Objective of my PhD programme;
The framework of SensorART project;
Topic of my current activity:
    Auto-Regulation Unit (ARU): a portable device for controlling LVADs;
Work done and results;
Work in progress.
Contents

## Slide 3
  Main objective
  to make a flexible sensorized platform
    based on commercial or research devices and sensors;
    acquiring physical, physiological and biochemical data;
    applications: the cardiovascular field, for monitoring patients with cardiovascular problems (e.g.: patients with failing heart).

## Slide 4: A remote controlled Sensorized ARTificial heart enabling patients empowerment and new therapy approaches

## Slide 5
  Current activity
  Auto-Regulation Unit (ARU): a portable device for controlling LVADs and…
task1
data acquisition
and management
data transmission to
Patient interface
VAD setting
and
monitoring
ARU
task2
task3
Power management
/alarms generator
task4
task5
Plug-in for a custom
User Control Interface
(UCI)
hardware evaluation and debug
(FPGA architecture)
Notes: As understandable from its complete name, it is worth mentioning that the ARU is not only a portable device which allows the user to control the LVADs status, but also it is able to store data (thanks to internal memories), which came from the MagIC shirt (belonging to the wearable platform) and implantable platform by the use of two communication protocols (serial and bluetooth) implemented in VHDL. It is able to transfers data to the external world via bluetooth communication (also implemented in VHDL), therefore it is a data-bridge towards the PMA(Patient Monitoring Application) too and so towards the SMA (Specialist Monitoring Application). In addition it is able to monitor the energy consumption and generate alarms. Finally, it is interfaced to the UCI (User Control Interface) which has to be used as a local controller which exclude the wireless link to the PMA (which remains the main path). By the use of the UCI, the user sets the pump speed and visualize the parameters of the pump.
An FPGA architecture (programmed in vhdl, hardware description Language) was selected in order to increase system flexibility and efficiency in running parallel multiple tasks;

## Slide 6: The core of a sensorized platform
Portable ARU
In-vitro
platform
Wearable
platform
Patient Interface
UART
Bluetooth
RS232
UCI
Connector
ARU

## Slide 7: The ARU hardware
Main characteristics:
Embedded and portable unit;
FPGA based board;
plug-in for a custom User Control Interface (UCI) for the local control of the VADs;
bluetooth link towards the PMA;
RF Link towards the implantable platform.
hardware evaluation and debug
Main functionalities
Proportional-Integrative (PI) control of the pump speed;
monitoring and acquisition of the pump speed and current;
monitoring of the sensor data (implantable and wearable data);
threshold control of the flow and pressure values by generating alerts;
control on the pressure variations with alert generation.
Notes: An FPGA architecture (programmed in vhdl, hardware description Language) was selected in order to increase system flexibility and efficiency in running parallel multiple tasks;

## Slide 8: Implantable Platform: in-vitro setup
Objective:
demonstration of the auto-regulation principle and feasibility;
to emulate the function of a sensorized VADs.
  Work done and results:
  Assembly of the several components;
  Millar sensors integration and its calibration;
  Electronic Signal conditioning (evaluation and debug);
  Acquisition of flow and pressure data at different pump speed, in order to assess the effective behavior of the platform in working conditions;
  Test on the ARU control algorithms;
In-vitro platform and ARU
ARU
PMA
Flow
Speed
Power
bluetooth
  Integration test on the communication protocol between in-vitro/ARU and ARU/ PMA interfaces;
Notes: The primary goal of the in-vitro implantable platform is the demonstration of the auto-regulation principle and feasibility. Moreover it will be also used as a test bench for components under development.

## Slide 9: Wearable Platform
Objective: monitoring of VAD implanted patients in the post operation phase with a platform,
  VAD-independent;
  Able to monitor as many physiological signals as possible (MagIC system);
  Comfortable and easy to be used.
ARU
UART
connection
Work done and results:
  Implementation (VHDL code) of the communication protocol of the MagIC/ARU interface;
  Integration and testing (MagIC/ARU interface);
  Programming of bluetooth for the data transfer ARU/PMA ;
  Test on the communication protocol of the MagIC/ARU and ARU/PMA interfaces.
ARU
MagIC
PMA
UART
bluetooth
MagIC
data
MagIC
data

## Slide 10: Work in progress: UCI
Objectives:
the specialist dedicated interface;
the back-up solution to real-time visualize data and to set the desired pump speed.
Work done and results:
Integration ARU/UCI;
Control of the UCI LCD (VHDL code).
ARU
UCI
UCI

## Slide 11
Thanks
for your attention