## Slide 1: Propulsion of a Robotic Hydro- Colonoscope Stuart Coleman Institute of Medical Science and Technology University of Dundee Surgical Robotics Summer School, Montpellier 10/09/13
Notes: Brief overview

## Slide 2: Background
Colorectal cancer is the third commonest type of cancer in the world
Screening improves survival, reduces incidence
Colonoscopy is gold standard for screening, but:
  Requires colonoscopist skill
  Patient discomfort
  Risks of complications
  Relatively expensive
Notes: There are over a million new CRC cases each year.
CRC develops from polyps on the inside surface of the colon. These can be detected byt screening and subsequently removed. If this screening process is carried out the survival rate of the cancer can be increased and the incidence can be reduced.
Procedure is difficult and high levels of skill are required for both insertion and inspection
Discomfort may require sedation, which complicates procedure and increases costs and disruptiveness, and may reduce attendance
Risk of perforation
Expensive compared to other screening options

## Slide 3: CODIR
Aims to develop a robotic colonoscope system to operate in a liquid-filled colon
Potential advantages are reduced patient discomfort and physician workload
Notes: CODIR project proposed to overcome some of these drawbacks.
Aims…
Using warm-liquid filled colon has been shown to reduce patient discomfort
Using a semi-automated system can reduce physician workload
Universities of Leeds and Dundee
ERC funded

## Slide 4: CODIR Team
My PhD Aims: Develop a propulsion system for use in robotic hydro-colonoscopy
My Status: In 1st 6 months of PhD project, part time.
My Supervisors: Prof. Cuschieri, Prof. Cochran
Notes: Work is a collaboration between the universities of Leeds (Mech Eng) and Dundee
PIs are Prof Anne Neville and Prof Alfred Cuschieri

## Slide 5: Hydraulic propulsion
Device driven by fluid pressure differential produced by external pump(s)
Balloons form sliding seals in colon lumen
Pressure transducers and magnetic position sensor for feedback
Similar to Aer-O-Scope
Notes: A device which is pushed through the colon by fluid pressure.
It forms a sliding seal on the inside of the colon and water is pumped in behind it so that it is pushed forwards.
Seals formed by two balloons which can be individually inflated/deflated to provide a conformable seal
Similar to aer-o-scope

## Slide 6: Initial testing
Tests in soft-embalmed porcine colon sections, constrained in straight or curved configurations
Manual and automated control feasible1
Pressure differential <4kPa (30mmHg)
1 Tapia-Siles S, Coleman S, Cuschieri A. Pipeline Inspection Gauge device for inspection of flexures during robotic hydrocolonoscopy. Paper presented at: 21st International congress of the EASES, June 2013; Vienna.
Notes: Flexures not negotiated with 100% success rate

## Slide 7: Questions
  Thanks for your attention
  Any questions/comments?
  s.y.coleman@dundee.ac.uk