## Slide 1: Lab N°3 Design for Testability
Notes: <number>

## Slide 2: Objectives
Realise the full synthesis flow
  Start from an existing design
  Use the synthesis tool « Design Compiler » from eSynopsys
  Use the test tool test « Tetramax » from Synopsys
<number>

## Slide 3: Design
A 8-bit filter
  Composed of an adder and two 8-bit register
  Source fille in the directory
    … /VHDL
<number>

## Slide 4: Synthesis
Tool dc_shell-xg-t (Design Compiler from Synopsys)
  Necessary scripts are available in the directory
    … /Synth
      .synopsys_dc.setup
      synthese_dc_shell.scr
<number>

## Slide 5: Test
Use Tetramax to generate test patterns
  Comment and analyse the obtained results in terms of testable and non-testable faults
  Comparer le TC avec et sans SCAN
<number>

## Slide 6: DfT
Modify the circuit by adding physically the scan path
  Use the tool dc_shell-xg-t
<number>

## Slide 7: Commands
Read the file
  read_verilog <ckt.v>
Specify the top module
  current_design <top module name>
<number>

## Slide 8: Commands
Specify the type of scan chain
  FF type
    set test_default_scan_style multiplexed_flip_flop
  Number of scan chain
    set_scan_configuration -chain_count <n>
<number>

## Slide 9: Commands
Add test input/output:
  Test_mode
  Test_si
  Test_so
  Test_se
  Create_port <name> -direction <in | out | inout>
<number>

## Slide 10: Commands
Specify the signals that are controlling the scan chain:
  Clock
  Set|reset
  Test_mode
  Test_si
  Test_so
  Test_se
<number>

## Slide 11: Commands
set_dft_signal -view exist -type ScanClock -timing {45 55} -port < clk >
set_dft_signal -view exist -type Reset -active_state 0 –port < reset >
set_dft_signal -view spec -type Constant -active_state 1 -port < test mode >
set_dft_signal -view spec -type ScanDataIn -port < test si >
set_dft_signal -view spec -type ScanDataOut -port < test so >
set_dft_signal -view spec -type ScanEnable –port < test se >
<number>

## Slide 12: Commands
Create the test protocol
  create_test_protocol
Add the scan chain
  dft_drc
  preview_dft
  insert_dft
Visualize the scan chain
  report_scan_path
<number>

## Slide 13: Commands
Save the test protocol
  write_test_protocol -o < file.spf >
Save the modify circuit
  write -format verilog -hierarchy –output < ckt.v >
<number>

## Slide 14: Test
Use Tetramax to check if the test protocol and the circuit with the scan chain are correct
Generate test vectors and save them
<number>